Input	Type	Outputs
5 0	On_Off	6 2	C 2
5 1	On_Off	C 3
5 2	Toggle	C 4

LCD Shield

Servo 0

Servo 1

      1a 0a
Output Module
8

        3b 3a 1b 0b

Output Module
6
3b 0a
    3a 2b 2a 1b 1a 0b

Output Module
C
3b 4a
3a 2b 2a 1b 1a 0b 0a 4b

Controller
Uno

Input Module
4

    3 2 1 0

Input Module
5

    2 1 0
4 0	On_Off	8 3	8 0	. 1	8 1	C 0	C 1
4 1	On_Off	8 3	C 2	. 1	8 1
4 2	On	6 1
4 3	Off	6 1

Lock	Lo 6 2	Hi 8 0	Lo 8 1

### Demonstration
1. Toggle 5 2	Opererates red/green bi-colour LED C 4.
2. On_Off 5 0	Operates red/yellow LEDs 6 2.
   Also operates red/green bi-colour LED C 2.
3. On 4 2	Operates 4-colour LEDS 6 0 and 6 1.
   Only issues “Hi” actions.
4. Off 4 3	Operates same 4-colour LEDS 6 0 and 6 1.
   Only issues “Off” actions.
   Also show automatic “Lo” action.
5. On_Off 4 1	Operates servo 8 1 and associated blue pad LED 8 1.
   Pad LED changes state when servo is half-way through it’s travel (not necessarily 90°).
   Also operates red/white LEDs 8 3 and blue/yellow flashing LEDs C 1.
   There’s a delay between the servo and the red/white LEDs 8 3.
   Flashing LEDs finish in the oposite state to where they started.
   Operation is reversed when going the other way.
6. On_Off 4 0	Operates servos 8 0 and 8 1 with a delay between them.
   Servo 8 0 represents a signal with a stutter when pulled, and bounce when released.
   Also operates the associated blue pad LEDs (at half-servo travel).
   Also operates LEDs C 0 and C 1.
   Multiple buttons have operated (some of) the same outputs.
7. On_Off 5 1	Operates Blink LEDs C 3.
   Just like flashing, except they go out after an interval rather than stopping on one colour.
8. LED 6 2	Locked hi if servo 8 0 is hi, or servo 8 1 is lo.
   Also, servos are locked if LED 6 2 is lo.
9. Multiple	Multiple simultaneous inputs can be actioned – eg to get more than 6 output actions.
   Different inputs can cause the same outputs to change – or a sub-set. Eg for multiple mimic panels.

### Configuration
1. Reset	Shows splash screen with software version.
   Shows connected input nodes.
   Shows connected output nodes.
   Initialises the input nodes – communicates with the MCP23017s to set them to input mode.
2. Calibrate	First run, or if any other shield button held during boot, calibration of buttons is performed.
3. Menu buttons.	Up or down to change option or increase/decrease setting.
   Left to go back (cancel changes), right to go deeper.
   Select to test/check current selection, or to save changes.
4. Output menu	Select node and pin.
   Select button to check/identify output.
   Choose output type.
   Adjust servo 8 0.
   Adjust LED 8 2.
   Left button to cancel, select to save.
5. Input menu	Select node and pin.
   Action with select button to check/identify associated output(s).
   Choose input type for On_Off 4 1.
   Select button to check/identify output.
   Select A, adjust pin and check/identify output.
   Select B to show flashing LED C 1.
   Select C to show delay – select button on node number.
   Set delay to zero.
   Left button to cancel, select to save.
6. Export menu	Show export output.
7. Import menu	Import some definitions.
8. System menu	Report level.
   Nodes.
9. Lock menu	Show lock for LED 6 2 (Lo) vs servos 8 0 (hi) and 8 1 (Lo).

### Miscellaneous
1. Reset	Software version blinks on built-in LED.
   Output modules also blink their ID.
2. Renumber	Renumber module.
   How to reset to manual jumper-setting.
3. Scan inputs	To select which input node/pin to configure.
4. EzyBus	Auto-config of EzyBus configuration.
5. Road	Output type. Can work multiple ones

### Architecture
1. Inputs	Specification held in the Uno.
2. Outputs	Specification held in the relevant Nano.
3. Multi-tasking	Main loop decides which functions need to run based on timers.
4. PWM	By hand, with care taken to power LEDs on opposite phase. Lower current and can use common dropper resistor.
### Code
1. Loop	How multi-tasking is achieved.
   Also in output module software.
2. Receipt	Receipt of commands.
   Stores for actioning by the main loop – interupt response must be quick.
3. Request	Receive the command for data and store it.
   Respond when request for data arrives.
4. Servo steps	Control structure to keep track of servo’s position.
   Initial setup from an “action” command.
   StepServo method.
5. LED steps	Similar method to servos for fading, but much faster.
6. Remote store	Output configurations are held in the output modules.
   Need more space.
   Local to usage.
   Easy to avoid servo twitch at start-up.
7. Libraries	Minimal dependency of libraries – size and functionality concerns.
8. Git	Record of changes with divergent development.
   Bitbucket rather than GitHub at present.