Extending EzyBus

# Summary
I'm attempting to provide more functionality using the EzyBus hardware but with completely re-written sketches.
My motivation is that I love the simplicity of EzyBus, both the hardware build and the operation, but I wanted more features. However, a CBUS solution has much more complexity than I need so this is a half-way house.
A second driver is that as an ex-software developer, I wanted to see how arduinos operate and have a go at programming them.
I realize a big advantage of EzyBus is how easy it is, and my changes are necessarily going to be “not so easy”. I have no intention of stepping on EzyBus's toes, this is not an EzyBus solution, but a solution using the EzyBus hardware, that is: an arduino Uno with LCD shield, some nanos and MCP23017s mounted on the kitlocker PCBs all connected by I2C bus.
## Features
The features I want to include (if I can) are:
- Different types of input in addition to the toggle-switch - in particular, intermittent (non-latching) push buttons.
- Multiple inputs can be operated simultaneously.
- Multiple outputs operated by a single input - eg crossovers.
- Multiple inputs operate the same output(s) - so multiple mimic-panels can control the same outputs.
- In addition to servo outputs, variable-intensity LEDS (including fading) using PWM.
- Some other output types, eg flashing (varying speeds) or flickering LEDs.
- Where multiple outputs are controlled by an input, the ability to delay the outputs, so for example crossing gates can operate one after the other.
- Interlocks that prevent certain outputs operating if other outputs are set incorrectly.
## Background
My current layout is in 009 (DCC) and half of it is operated by fulgurex slow-action point motors operated by SPST toggle switches and some 2-aspect colour signals (also operated by SPST toggles).
The point motors are too noisy for my liking and the underside of the board is rapidly becoming a rats-nest of wiring. The second half of the layout is not wired yet, and having seen the MERG stand at a railway show decided to join and see what options there are.
I've built some MERG kits (CANPAN kit 9, CANTM7 kit 497) but had a lot of difficulty with the SMD devices (my soldering skills not being up to the task) and failed to get them working as a result. I also took a look at the FCU software but wasn't impressed - it has a very steep learning curve. I then found EzyBus on the MERG website and decided CBUS was too much for my needs but unfortunately EzyBus was to restricted, so I'm now looking at a half-way house.
My intention is to wire the second half of the layout with servos and an extended EzyBus-based mimic panel, and if successful, replace the fulgurex motors and their control panel similarly. There'll be two control panels (one on each side of the layout) and some (all?) functionality duplicated on both panels.
## Hardware
I'm using the EzyBus PCBs from the kitlocker (kits 922 and 923) built exactly as described in the ezybus manual. I sourced all the components as there was no EzyBus kit at the time.
With the MCP23017 I had two minor problems. There are SPI and I2C variants and I wasn't sure I'd got the right one. As the writing on the chip was illegible, and its PCB was labelled both MCP23017 and MCP23S17 I just used it anyway (and it was an I2C one). Secondly, the one I bought had 1/10th inch wider spacing between the two rows of pins. So rather than using rows of sockets and pins I soldered the MCP directly to its PCB using bent pins to line them up.

## Progress
I have most of the features I want coded and working on a test-bed.
In addition to the desired features I've also implemented:
- Four-aspect signals.
- Rudimentary signal-bounce.
- Automatic reset of inputs after a time delay (for signals that go red/danger with input from a TOTI but then revert to green sometime later).
I've pretty-much maxed-out on the space available in a Uno (only 3k program space left) so may have to move to a mega if I think of any more functionality. The nano output modules have plenty of room for expansion.
The next step will be to install something on the layout to see how well it works in reality.
# Overview
The system consists of an Arduino Uno controller, up to eight input modules (MCP20913 chips) and up to 16 output modules (Arduino nanos) all connected by an I2C 2-wire bus.
The inputs are not directly tied to the corresponding output. Each input can be mapped to operate any output. Indeed, each input can operate up to seven outputs simultaneously or in sequence.
The outputs generally drive servos with an associated digital output, or a pair of digital outputs (often LEDs). For servos, the range of rotation (or reverse rotaton) and speed of rotation can be specified. The digital outputs use PWM so can arrange to fade and/or dim the outputs.
Interlocks can be specified between outputs to prevent certain combinations, for example prevent a signal being cleared if the points are set incorrectly (and vice-versa).
## Inputs
Each input module provides 16 input lines which are normally held high. Pulling the input low activates the input.
Each input can be configured to operate in one of four types:
Toggle	An on-off toggle switch (eg SPDT). Switched high sets the corresponding outputs “Hi”, switched low sets the outputs “Lo”.
On/off	A momentary push-button. First activation sets the output “Hi”, another activation sets the output “Lo”.
On	A momentary push-button which always sets the corresponding outputs “Hi”.
Off	A momentary push-button which always sets the corresponding outputs “Lo”.
## Outputs
Each output module has 8 outputs which can be configured as one of six types.
Servo	Output connected to a servo which can rotate between 0-180 degrees. The endpoints can be set, as can the speed of rotation.
Signal	A servo as above which additionally emulates bounce typical of a semaphore signal.
LED	A LED or other digital output device, typically a (2-aspect) colour signal.
LED_4	A 4-aspect colour signal.
Flash	A pair of LEDs that flash for a while whilst changing state – one ends up on, the other off.
Blink	As for Flash above, except that the output always ends in the off state.
The output modules have three-pin headers for connection to servos (Signal, Vcc and Ground). There’s an additional digital output (“pad”) which goes high when the servo is “Hi”. When connecting digital outputs (LEDs) the main output is on the servo “Signal” pin, with a complimentary output an the associated “pad” output.
# Setup
Having connected all the devices (Uno, input and output modules) to your I2C bus and suitable power supplies, switch everything on.
The Uno will display its splash panel on the LCD.
 SignalBox v2.6
 Setup Jan 21

After a few seconds, a prompt to calibrate the LCD buttons appears. Press the indicated buttons in turn as prompted.
 Calibrate button
 Press select
Now a display indicating the attached input and output modules. The top line shows the numbers of the input modules detected (numbered 0 to 7) or a dot for missing modules.
 Nodes ....4...
 .....5..8.......
The second line shows the output modules detected (numbered in hexadecimal from 0 to f). In the example, input module 4, and output modules 5 & 8 have been detected.
Next a message indicating the input nodes are being initialized.
 Init
 ....4...

When complete, the standard panel is displayed showing the time the software has been running which gives confirmation that the software is running OK.
 SignalBox v2.6 00:12 Jan 21
This is the normal running state for the software. After this initial setup, subsequent boots of the software will progress directly to this panel. No further interaction is required.
# Configuration
To enter configuration mode, press any of the LCD buttons and the configuration menus are shown.
## Menu buttons
The menus are navigated using the LCD buttons.
Up	Moves to the next menu at the current level, or increases the value of the current field.
Down	Moves to the previous menu at the current level, or decreases the value of the current field.
Right	Selects the current item and moves to the sub-menu or next field.
Left	Exits the current item and moves to the next higher field or menu. If changes have been made, then confirmation is request that they should be discarded.
Select	Depending on the context, one of three things may happen:
    1. The current changes are saved. A warning message is displayed to confirm the changes made. If no changes have been made, operates as the “Left” button.
    2. The current item is toggled between it’s normal state and an alternate one (eg output is disabled/enabled).
    3. The current item is exercised so you can identify the output, or check the changes you’ve made are those desired.
      The currently selected menu or item is marked at all times with chevrons – the ‘>’ and ‘<’ characters.
## Menu structure
The top-level menu has 6 options.
 System< v2.6 Report Long
The example image shows the System menu selected with its current sub-menu also displayed.
System	Configure system-wide options.
Output	Configure the output modules.
Input	Configure the input modules.
Lock	Configure interlocks between outputs.
Export	Export the current configuration.
Import	Import a previously saved configuration.
Use the up/down buttons to select the desired sub-menu and the right-button to enter the selected one.
When returning to this menu (if changes have been made) using the left (to cancel) or select (to confirm) buttons, a warning message is displayed asking for confirmation.
 System v2.6 Confirm? Sel=Yes
When the warning message appears, use the select button to accept or any other button to refuse, the cancellation or confirmation of the changes as desired.
### System menu
The system has four sub-menus:
Report	Sets the reporting level.
Debug	Sets the debug level.
I2C	Sets the I2C node IDs for the control module, and the base node ID for the input and output modules.
Nodes	Displays the detected input and output modules node IDs (as shown during startup).
Use the up/down buttons to select the desired sub-menu, and then right-arrow to enter the sub menu configuration.
Use the left or select buttons to cancel or confirm any changes and exit.
#### System report sub-menu
This allows the reporting level to be set. When inputs are triggered and outputs actioned, this level dictates what messages (if any) are shown on the LCD panel.
 System v2.6 Report< Long
Use the right-button and then adjust the level using the up/down buttons.
 System v2.6 Report >Brief <
None	No reports are shown.
Brief	Reports are shown for a brief period (about 2 seconds).
Long	Reports are shown for a long period (about 4 seconds).
Pause	A report is shown and the operator must acknowledge it before any more processing can continue by pressing one of the LCD buttons.
#### System Debug sub-menu
This controls the verbosity of debug messages output to the serial port of both the Uno control module and the output modules.
 System v2.6 Debug < Brief
Use the right-button and then adjust the level using the up/down buttons.
 System v2.6 Debug >Detail<
None	No debug messages are output.
Error	Only error messages (when something goes wrong) are output.
Brief	Brief messages describing major events are output.
Detail	More detailed messages are output for more events.
Full	Debug messages are output for all events.
#### System I2C sub-menu
Allows the I2C node numbers to be adjusted. This should never be necessary during normal operations.
 System v2.6 I2C < 20 30 50
The second row shows the currently-set IDs (in hexadecimal).
Use the right-button to select the desired field to edit, and the up/down buttons to alter the values.
 System Con I2C >20<30 50
Con	Sets the controller’s I2C node ID.
Inp	Set the base ID of the input modules.
Out	Set the base ID of the output modules.
#### System Nodes sub-menu
Shows the connected input and output module node numbers.
 System v2.6 Nodes <
Use the right-button to show the node IDs.
The example shows input nodes 1 & 4, output nodes 5 ,8. and ‘f’.
 Nodes .1..4...
 .....5..8......f
No changes can be made.
### Output menu
Configure the outputs. The second row shows a summary of the selected output’s current configuration. These are its type, the “Lo” and “Hi” settings and the servo speed, all in hexadecimal.
 Output< 4 1 Servo 4f 3e d
Use right-button and then select the module ID to configure. Use the right-button and then select the individual pin to configure.
 Output 4 >1< Servo 4f 3e d
Use the right-button again to move to the type field. Use the up/down buttons to select the desired output type.
 Output 4 1 Servo <4f 3e d
#### Output Servo sub-menu
Use the right-button to configure a servo’s movement positions and speed.
 Output Lo Hi Servo > 79< 62
The servo’s Hi and Lo positions are now shown as decimals between 0 and 180 (degrees).
The servo will move in sympathy to the changes made. Use the select button to test the servo, it will move between the specified Lo and Hi positions.
Use the right button to move to the “Hi” field. The servo will move to the Hi position at the same time.
 Output Lo Hi Servo 79 > 62<
Again, the servo will move in sympathy to the changes made. Again the select button will test the servo.
Use the right-button to configure the servo’s speed.
 Output Spd Reset Servo >d< 0
Speed ‘0’ is the slowest, about 1.5 seconds, ‘f’ the fastest (as fast as the servo can go).
Use the right-button to configure the reset interval. This the time (in seconds) after which the servo will automatically return to its Lo state. Zero means don’t auto-reset.
 Output Spd Reset Servo d > 0<
Use the left-button to return through the fields to the “Servo” field.
Use the left or select button to cancel or confirm the changes.
#### Output Signal sub-menu
Signals operate in exactly the same manner as servos above.
 Output 4 2 Signal<5a 87 e
All the same features are available.
#### Output LED sub menu
Use the right-button to configure LED’s intensity and speed of change. PWM is used to vary the intensity.
 Output 4 2 LED <3f 3f d
The LED’s Hi and Lo intensiities are now shown as decimals between 0 and 255.
The LED’s intensity will vary in sympathy to the changes made. Use the select button to test the LED, It will go out and the complimentary LED will illuminate (at the Hi intensity).
Use the right button to move to the “Hi” field. The LED will go out and the complimentary LED will illuminate (at the Hi intensity).
 Output Lo Hi Servo 79 > 62<
Again, the LED will move in sympathy to the changes made. Again the select button will test the LED.
Use the right-button to configure the LED’s speed.
 Output Spd Reset Servo >d< 0
Speed ‘0’ is the slowest, taking about 1.5 seconds to illuminate or extinguish. The fastest speed is ‘e’, about a tenth of a second. Speed ‘f’ makes the LED flicker randomly.
Use the right-button to configure the reset interval. This the time (in seconds) after which the LED will automatically return to its Lo state. Zero means don’t auto-reset.
 Output Spd Reset Servo d > 0<
Use the left-button to return through the fields to the “LED” field.
Use the left or select button to cancel or confirm the changes.
#### Output LED_4 sub menu
LED_4 outputs are configured in exactly the same manner as LEDs above.
 Output 4 3 LED_4 <3f 3f d
All the same features are available.
#### Output Flash sub menu

#### Output Blink sub menu

### Input menu

### Lock menu
### Export menu
### Import menu

## Inputs
Each input module provides 16 input lines which are normally held high. Pulling the input low activates the input.